## Slide 1
FHO5000 PRO Improvement
PRO version serial number start with E5FHA2xxxx
1: Dynamic range improvement
2: Deadzone optimization
3: FLM(Fiber linke map) performance optimization
4：Add some New functions

## Slide 2
1：Dynamic range improvement
Based on the improvement of hardware circuits and APD circuits, the dynamic range performance of (3ns-20us) has been comprehensively improved, especially with significant improvement in small and medium pulse width dynamics. (for example: OTDR can have 7dB dynamic even at 3ns)
old version at 3ns
new version at 3ns

## Slide 3
old version at 10ns
new version at 10ns
1：Dynamic range improvement

## Slide 4
1：Dynamic range improvement
old version at 1us
new version at 500ns

## Slide 5
1：Dynamic range improvement
old version at 20us
new version at 20us

## Slide 6
200km fiber optic measurement in lab environment (FHO5000-D45PRO)
1：Dynamic range improvement
50km fiber optic measurement with 500ns in field
(FHO5000-D45PRO)

## Slide 7
2: Deadzone optimization
New Event deadzone：<0.8m
New attenuation deadzone：<3.5m
⭐Easy detection of 2 meters continuous patchcord
and fiber attenuation within 10 meters

## Slide 8
Min 30m
✔
Based on improvements in hardware circuits and software, dynamic enhancement, deadzone reduction, resulting in a comprehensive improvement in FLM(fiber link map) testing performance
A : More precise FLM testing performance, shorter 30m PON deadzone when testing non reflective splitter link
B : Maximum can test through 1x128 splitter， for example 1x16+1x8 splitter
1x8
1x16
1x16
✔
Min 80m
1x8
1x4
Min 80m
✔
1x8
3: FLM performance optimization

## Slide 9
FLM PON testing Sample: Two ratios splitter
3: FLM performance optimization

## Slide 10
3: FLM performance optimization
FLM PON testing Sample: One ratio splitter

## Slide 11
FHO5000-T40F/T43F/T45F PRO added built-in optical fiber (about 30m) which enable it can test splitter directly without connecting launch cable
3: FLM performance optimization

## Slide 12
A：The new version added a new testing mode: 1x? When the splitting ratio of the splitter is unknown, the user can choose 1x? test mode
B：launch fiber and end receiving fiber can be set
C：Add FLM PON diagram
3: FLM performance optimization
FLM Setting Interface
Some new function
1: Generate FLM PDF report
2: Print screen as bmp format
3: Modify wrong fiber event
4: Convert to OTDR trace

## Slide 13
4、New functions
The OTDR curve mode and FLM test mode support the judgment of Pass/Fail function, and the FLM mode also has fault diagnosis analysis
OTDR trace mode
FLM testing mode

## Slide 14
PRO version can directly generate OTDR PDF reports and FLM PDF reports without the need for computer software to generate reports
4、New functions

## Slide 15
FHO5000 PRO support bluetooth and android mobile phone app
4、New functions

## Slide 16
Gestures region zoom
Before ZOOM
After ZOOM
4、New functions

## Slide 17
Launch Cable function
1：Add end receiving fiber setting
2：there are two mode to set the start launch fiber and end receiving fiber
a： according to the pre-set fiber length
b：according to the event number
The middle part of the green dashed line is the actual line part
4、New functions

## Slide 18
Conversion of OTDR trace and Fiber link map
1: On the FLM testing interface, click trace to open the OTDR trace
2: OTDR trace and event map can displayed on the same screen together
4、New functions

## Slide 19
Modify wrong event type in OTDR trace mode
Sometimes the reflection of APC connections is very low, and OTDR may think it is a fusion point as non-reflection event.
4、New functions

## Slide 20
Modify wrong event type in FLM test mode
Sometimes the reflection of APC connections is very low, and OTDR may think it is a fusion point as non-reflection event.
4、New functions

## Slide 21
4、New functions
Bidirectional analysis function
Load the measurement results of a fiber link from both directions and perform analysis

## Slide 22
OLS PART： The laser source has added a modulation frequency output mode
4、New functions

## Slide 23
5: others
Change of optical port sequence
from left to right
optical 1310/1550nm port--VFL--OPM-- optical 1625nm port with filter
MM 850nm/1300nm port

## Slide 24
Thanks
Let’s go in the Grandway !